## Slide 1: DArk Matter Particle Explorer
Alfonso Cavallo

## Slide 2: Dark Matter
Galaxy Arms Speed
Unexpected errors in the estimate of galaxies’ arm speed can only be explained by DM
Universe Structure
Cosmological Structures’ theory hold only if DM is taken into account
Gravitational Lensing
Only DM can explain the Bullet Cluster’s gravitational lensins
DM mass
visible mass

## Slide 3: Ways of Detecting Dark Matter
Production
Interactions in particle colliders generate DM
Indirect Detection
Dark Matter interactions produce energy. Products from void areas can be a hint of Dark Matter existence.
Direct Detection
Dark Matter directly interacts with the detector and the produced energy can be measured

## Slide 4: The Messengers’ Connection
,…
Dark Matter can annihilate and produce rays or weakly interacting particles…
… or generate charged particles which may travel long paths and be deflected by interactions with matter

## Slide 5: DAMPE
Dark Matter Particle Explorer

## Slide 6: Sun-Synchronous Orbit

## Slide 7: Plastic Scintillator Detector (PSD)
https://arxiv.org/abs/1703.00098
884mm
28mm
10mm
PMT
8mm
Position Resolution: 6mm
Charge Resolution: 0.25 for Z=1

## Slide 8: Silicon-Tungsten Tracker (STK)
121µm
9.5cm
9.5cm
121µm
9.5cm
9.5cm
320µm
Tungsten
γ-ray conversion
X
Y
Position Resolution: 80µm
Angular Resolution: 0.2° for E=10GeV
~7 m2

## Slide 9: Bismuth-Germanium Oxide calorimeter (BGO)
14 alternated layers (divided in X and Y direction).
Each layer is a plane of 22 BGO bars with a section of 2.5cm x 2.5cm and a 60 cm long.
Each bar is read by PMT.
Electromagnetic Energy Resolution: ~1.5% above 100GeV
Hadronic Energy Resolution: ~40% above 800 GeV

## Slide 10: Neutral Detector (NUD)
Improved Electromagnetic and Hadronic showers separation
The NUD is designed to detect delayed neutrons which normally arrive 2µs after the shower collides with the BGO
Boron-loaded plastic
PMT

## Slide 11: Fully-Assembled System
Mass: 1900Kg (Payload 1,480 kg)
Power: 850W
Downlink Data rate: 12 GB/day
Expected lifespan: 3 years

## Slide 12: Ground Calibration Tests
Argon Beam fragments’ charge measurement test (PSD)
Electron’s Energy reconstruction test
Proton’s Energy reconstruction test from BGO heat (5, 10, 150, 400 GeV/c)

## Slide 13: In-Flight Performance Test
BGO deposited energy for Helium
PSD deposited energy for proton
Trigger Detection w.r.t lat/lon
South Atlantic Anomaly

## Slide 14
Dead Time | On-Orbit Calibration | Solar Flare | South Atlantic Anomaly
Time required for processing | Time required for calibration | Exceptional Event (09/09/2017-13/09/2017) | Time spent passing over the SSA
~17.2% | ~1.7% | ~0% | ~4.9%
GCR Measurement (Time Filtering)
The total time considered is (roughly 1157 days of acquisition) an it is
Approximately 76.2% of the total operative time

## Slide 15
GCR Measurement (Pre-Selection)
Fixes geomagnetic
cut-off
Minimum Energy for a resolution in in the band
of the layers 1 and 2 shall be greater than the in the layer 3 and 4.
Filters out all GCRs not coming from the direciton of observation
Effectively removal of particles coming from the side
BGO

## Slide 16
GCR Measurement (STK Selection)
Filtering out the tracks with less than 3 hits
Selection of the fittest track
Verification of coherence with the BGO track
Verification that the track is fully contained in the PSD, STK, BGO
1
2
3
4
STK
BGO
BGO Projected Track
STK Projected Track
PSD
For all the layers of the PSD
For the first 4 layers of the BGO

## Slide 17
GCR Measurement (Helium Filtering)
The isolation of Helium charges is carryed out by selecting only charges at the first STK hit that are measured to be at least higher than 2.5 the proton MIP-equivalente signal.
A further selection in both the PSD layers (X and Y) was performed to take into account energy-dependency at different particle energy ranges:

## Slide 18
GCR Measurement (Results)
An hardening of the Helium spectrum was predicted with high uncertainties at ~ TeV.
Was able to perform direct measurements of that spectrum, confirming the results.
As it can be noticed in the plots there is an actual hardening of the Helium Spectrum at ~0.9 TeV with a softening at ~ 30 TeV.
This results have huge value for GCR research.

## Slide 19: DAMPE directly confirms the Helium spectral break!

## Slide 20: Other Contributions of DAMPE
During its many years of operativity, DAMPE has provided data about many different phenomena, including but not limited to:
Electron/Positron spectrum measurements;
Cosmic Rays Charge Measurement;
Helium Spectrum measurement (25 GeV – 4.6 TeV);
Geminga and Vela Pulsars’ periodicity measurement (1-100 GeV);

## Slide 21: THANKS FOR YOUR ATTENTION